Connectivity
a subsystem of the diagnostics project
by
Tiffany Gallops

A.	Connectivity refers to the connection between a PC or stand alone device to another PC or stand alone device. The connection allows communication and the transfer of data between the two devices. There are a great many ways to connect two or more devices using either a wired or wireless connection. Wired connections run a wire between the two devices to transfer data. The most popular wired connection by far is the USB port. It runs a wire between the two devices, or a point to point connection, and transfers data through the wire. Wireless connectivity has a couple more options. The more popular ones are bluetooth, zigbee technology, and WiFi. Bluetooth technology is geared toward voice and data applications and operates on an unlicensed 2.4GHz bandwidth. It can operate fine, depending on the quality of the hardware, at a distance up to 100m. The technology is able to penetrate solid objects, like walls, and is omni-directional, meaning it does not need to be in line of sight with the device to which it is transferring data. Best of all, bluetooth technology is low cost, with most bluetooth chips costing just under $3. Zigbee technology is a relatively new wireless connection formally adopted at the end of 2004. It's specifications are very similar to bluetooth, but is geared more for the industrial field. Zigbee does not have very high data transfer rates, but it makes up for that with low power consumption, low cost, and ease of use. Wi-Fi is a wireless connection used to test and certify 802.11 based wireless equipment. Although relatively popular, bluetooth costs a third of the price to implement and uses a fifth of the power Wi-Fi consumes.

In order to make the project work, some sort of connection is needed in order to transmit data from the black box monitoring device to the PC to be monitored. The client has specified that wireless Bluetooth technology be implemented into the device. According to www.bluetooth.com, Bluetooth is a wireless communication link, operating in the unlicensed ISM band at 2.4 GHz using a frequency hopping transceiver. It allows real-time AV and data communications between Bluetooth Hosts. The link protocol is based on time slots.

B.	The most basic core of a bluetooth device consists of a RF transceiver, baseband controller and protocol stack. All other components are optional, giving manufacturers variety when building bluetooth devices. Almost all Bluetooth wireless connections use low power consumption, are low cost, and have relatively high security. There are several different ways to implement Bluetooth hardware into the diagnostics tool. One way is through modules. Bluetooth modules are completely self contained systems, with an interface that connects with other components of the circuit. Most hardware modules can be dropped in the circuit and loaded into the system, making them easy to use. Another way is with an Integrated Circuit (IC) chip. Integrated circuits are normally just referred to as chips and are circuits that have been etched onto tiny chips of silicon, or semiconductors. They can perfom very basic input and output functions and work best with the connectivity system as a whole. Integrated Circuits can be used in a variety of devices, including computer hardware like the microprocessor and in audio and video equipment. A more advanced type of IC chip is the Multi-chip Module. According to wikipedia, a Multi-Chip Module (MCM) is a specialized electronic package where multiple integrated circuits or other modules are packaged in such a way as to facilitate their use as a single IC. The MCM itself will often be referred to as a "chip" in designs, thus illustrating its integrated nature. This sort of “chip” would allow for more complex functions than just a regular IC chip. Finally, most Manufacturers of IC chips and modules, and even manufacturers of Connectivity technologies offer a Development Kit, which is essentially a complete kit, with circuit board, antenna, and all necessary hardware and software needed to piece together a legitimate connectivity solution. However, most development kits can run between $200 and $400 U.S., which is too far out of range for the budget of this project. The optimal choice for the project would be to use a module to connect the device to the monitored PC.

Architecture of a Bluetooth Device.

C.	The following examples are possible bluetooth devices that could be implemented into the project. Entire Development kits are available for Bluetooth, including hardware and the software needed to program the device. Modules and Integrated Circuit, or IC, chips are also being considered, which include all the necessary hardware, just not the software.

Cambridge Silicon Radio (http://www.csr.com/) offers a Casira Bluetooth Development kit. It's a single IC chip solution for bluetooth implementation, integrating a 2.4GHz radio, baseband controller, and microcontroller all on one board. The chip uses bluecore7 technology, which is the most advanced chip for bluetooth, and meets low energy consumption standards. No price is listed, but the company can be contacted for sample chips and any additional information.

Bluecore7 specifications:
Bluetooth version 2.1
Bluetooth Tx output power +10dBm*
Bluetooth Rx sensitivity -93dBm*
Process geometry 90nm Chip area 11.7mm2
External component count (eBOM) 10 or fewer
Low ‘page scan’ power 0.45 milliwatts
AuriStream® power (EV3)1 11 milliwatts
CVSD power (EV3)1 19 milliwatts
HV3 operating power 18 milliwatts*
Standby power 40 microwatts*
* Simulated typical values

National Semiconductors (http://www.national.com) sells connectivity processors, or modules, with bluetooth baseband integrated circuits. Two modules that the company sells are of interest to this project. The LMX5453 is a micro module with integrated bluetooth 2.0 baseband controller and a 2.4GHz radio. The LMX9838 is a serial port module with bluetooth 2.0 baseband controller and a 2.4GHz radio. The full serial port bluetooth node also includes an antenna. The LMX9838 qualifies as a bluetooth endproduct, meaning it is ready to be used as an application without additional testing. The LMX5453 supports communication with a USB interface and features point to point management, transferring data at a rate of 723Kbps. Although samples are offered with a request to the company, a complete evaluation kit can be purchased for just under $200.

The bluegiga website (http://www.bluegiga.com) is another company that offers modules with bluetooth capabilities. Two similar module models that were of interest to the current project were the WT11 and the WT12. The WT11 boasts a radio, antenna, and fully implemented protocol stack. The module is USB 2.0 compliant and is pin to pin compatible with the WT12. The WT12 class 2 Bluetooth 2.0 EDR module has an Integrated chip antenna, comes with complete development, testing, and verification services, and contains everything from the radio to the antenna. Both modules are based on the csr bc04 chipset. The IC bluecore chip, manufactured by LM technologies, runs at between a 3V to 3.6V power operation and is fully compliant with the Bluetooth 2.0+ EDR specifications.

Csr bc04 IC chipset

Sparkfun (http://www.sparkfun.com) offers their own module based on bluetooth technology. The Bluetooth DIP module is a serial port module that is based off of the bgb203 IC chip, made by NXP semiconductors, which provides complete plug and play operation and is sized below 50nm². The chip has also been packaged in such a way that it requires no RF layouts or external components. The module, with the IC chip, can transfer data at rates up to 1Mbps, has a low power sleep mode, and is compatible with bluetooth products that support SPP, or serial port profile.

Bluetooth DIP module