Connectivity

A.*Insert Abstract Here*

The client has specified that wireless Bluetooth technology be implemented into the device. According to www.bluetooth.com, Bluetooth is a wireless communication link, operating in the unlicensed ISM band at 2.4 GHz using a frequency hopping transceiver. It allows real-time AV and data communications between Bluetooth Hosts. The link protocol is based on time slots. The wireless technology is used mainly in voice and data applications.

B.	The most basic core of a bluetooth device consists of a RF transceiver, baseband controller and protocol stack. All other components are optional, giving manufacturers variety when building bluetooth devices. Almost all Bluetooth wireless connections use low power consumption, are low cost, and have relatively high security.

Architecture of a Bluetooth Device.

C.	The following examples are possible bluetooth devices that could be implemented into the project. Entire Development kits are available for Bluetooth, including hardware and the software needed to program the device. Modules and Integrated Circuit, or IC, chips are also being considered, which include all the necessary hardware, just not the software.

Cambridge Silicon Radio (http://www.csr.com/) offers a Casira Bluetooth Development kit. It's a single IC chip solution for bluetooth implementation, integrating a 2.4GHz radio, baseband controller, and microcontroller all on one board. The chip uses bluecore7 technology, which is the most advanced chip for bluetooth, and meets low energy consumption standards. No price is listed, but the company can be contacted for sample chips and any additional information.

Bluecore7 specifications:
Bluetooth version 2.1
Bluetooth Tx output power +10dBm*
Bluetooth Rx sensitivity -93dBm*
Process geometry 90nm Chip area 11.7mm2
External component count (eBOM) 10 or fewer
Low ‘page scan’ power 0.45 milliwatts
AuriStream® power (EV3)1 11 milliwatts
CVSD power (EV3)1 19 milliwatts
HV3 operating power 18 milliwatts*
Standby power 40 microwatts*
* Simulated typical values

National Semiconductors (http://www.national.com) sells connectivity processors, or modules, with bluetooth baseband integrated circuits. Two modules that the company sells are of interest to this project. The LMX5453 is a micro module with integrated bluetooth 2.0 baseband controller and a 2.4GHz radio. The LMX9838 is a serial port module with bluetooth 2.0 baseband controller and a 2.4GHz radio. The full serial port bluetooth node also includes an antenna. The LMX9838 qualifies as a bluetooth endproduct, meaning it is ready to be used as an application without additional testing. The LMX5453 supports communication with a USB interface and features point to point management, transferring data at a rate of 723Kbps. Although samples are offered with a request to the company, a complete evaluation kit can be purchased for just under $200.

The bluegiga website (http://www.bluegiga.com) is another company that offers modules with bluetooth capabilities. Two similar module models that were of interest to the current project were the WT11 and the WT12. The WT11 boasts a radio, antenna, and fully implemented protocol stack. The module is USB 2.0 compliant and is pin to pin compatible with the WT12. The WT12 class 2 Bluetooth 2.0 EDR module has an Integrated chip antenna, comes with complete development, testing, and verification services, and contains everything from the radio to the antenna. Both modules are based on the csr bc04 chipset. The IC bluecore chip, manufactured by LM technologies, runs at between a 3V to 3.6V power operation and is fully compliant with the Bluetooth 2.0+ EDR specifications.

Csr bc04 IC chipset

Sparkfun (http://www.sparkfun.com) offers their own module based on bluetooth technology. The Bluetooth DIP module is a serial port module that is based off of the bgb203 IC chip, made by NXP semiconductors, which provides complete plug and play operation and is sized below 50nm². The chip has also been packaged in such a way that it requires no RF layouts or external components. The module, with the IC chip, can transfer data at rates up to 1Mbps, has a low power sleep mode, and is compatible with bluetooth products that support SPP, or serial port profile.

Bluetooth DIP module