Bluetooth Connectivity
Analog Input Subsystem
- Conditions input analog signals to be readable by analog to digital converter
- Accepts signals within -12.7 to +12.7 V, scales them to a 0 to 5 V range.
- Shifting and amplification is configurable by PC Software via Data-path Control Hardware

---
Analog Input Design Options
- Op-amps chosen over transistors for amplification; inexpensive and simplifies design
- Multiplexed resistors provide configurable scaling of input signals

---
Data-path Control Subsystem
- Regulates the flow of data from input modules to PC
- Serializes data for acquisition by PC Software
- Allows PC Software to manage control of input data

---
Data-path Control Diagram

---
Data-path Control Design Options
Microcontroller chosen as best control method:

---
Power Subsystem
- Provides power for hardware subsystems
- DC-DC converter provides power for:
  - Analog Input Subsystem
  - Data-path Control Subsystem
- Lithium-Ion battery powers Wireless Subsystem directly

---
Power Subsystem Design Options
- Lithium-Ion battery powers wireless chip:
  - WT32 has built-in Li-Ion charging capability
  - Battery can power this directly, simplifies design

---
Wireless Link Subsystem
- Enables wireless transmission of acquired signals to PC
- Wireless eliminates need for PC to be physically connected to diagnostic tool

---
Wireless Link Design Options
- WT32 Bluegiga chosen for wireless communication chip:
  - More expensive than other options but more functionality
  - Allows operation via programmable commands

---
PC Software Subsystem
- Acquires data from data acquisition hardware
- Provides a graphical user interface
- Allows control over data acquisition process
- Enables display of saved data

---
PC Software Diagram

---
PC Software Interface